Please submit documents to ACB as separate exhibits/documents in Adobe Acrobat PDF format

Required Exhibits for FCC Certification (FCC Rule Section 2.1033(b) – See Information Sheets and attachments for further explanations):

1.  	FCC ID – XXXYYYYY

XXX    = Grantee Code (3 or 5 characters as assigned by FCC);

YYYY = Product Identifier (maximum of 14 characters (A-Z, 0-9, -) assigned by applicant)

2.    FCC Registration Number (FRN)

3.    ACB Application Form (FCC) – Downloadable from

https://acbcert.com/documents/misc-docs/ACB-Form-731.doc

4.    Agency Authorization Letter.  Examples of Letter for FCC are downloadable from https://acbcert.com/documents/misc-docs/ACB-Form-FCC-Application-Letters.docx

5.    Theory of Operation/Technical Description

6.    Tune-Up Procedure

7.    FCC ID Label Artwork

8.    Label Location

9.    User’s Manual

10.  Block Diagram

11.  Schematics

12.  Parts List

13.  Confidentiality Request Letter - Please refer to

https://acbcert.com/documents/misc-docs/Memo-Short-Term-Vs-Standard-Confidentiality.pdf  for complete details.  Examples Confidentiality Letters are included in

https://acbcert.com/documents/misc-docs/ACB-Form-FCC-Application-Letters.docx

14.  External Photos

15.  Internal Photos

16.  Report of Measurements

17.  Test Setup Photos

18.  SAR (specific absorption rate) and/or MPE (maximum permissible emissions) data (if applicable)

(continued)

19.  Scanning Receivers – If applicable, a statement describing methods used to comply with design requirements of all parts of Section 15.121.

20.  Transmitters operating w/n 59.0 - 64.0 GHz band - exhibit showing compliance with 15.255(g) and (i).

Required Exhibits for Innovation, Science and Economic Development (ISED) Canada’s Certification, formally known as Industry Canada (RSP-100 – Documentation from above is required along with the ISED specific requirements below - See Information Sheets and attachments for further explanations):

21.  ISED ID - Company Number (obtained from ISED) followed by UPN (unique product number) up to 11 characters.

22.  ACB ISED Application Form, test report cover sheet, and letters (ISED) - Downloadable from our forms and docs section on

https://acbcert.com/documents/misc-docs/ACB-IC-Application-Form.doc &

https://acbcert.com/documents/misc-docs/ACB-IC-Test-Report-Cover-Sheet.doc &

https://acbcert.com/documents/misc-docs/ACB-IC-Application-Form-Letters.doc

23.  Name, Address and Contact Information of manufacturer if different from applicant.

24.  Agency Authorization Letter (Attached to ISED Letters above)

25.  RSS-102 Attestation (if applicable to device and attached to ISED Letters above)

26.  RSS-210 (or applicable rule parts that apply) Warning Statement for User’s Manual (if applicable to device).

27.  Canadian Point of Contact and Attestation Letter (must be located within Canada – may be authorized agent or distributor – Attached to ISED Letters above).

28.  ISED ID Label Artwork that also includes HVIN and PMN as applicable per RSP-100 (May be same label from FCC documentation if it also includes all of ISED’s requirements.).

(continued)

Below are further explanations and details some of the above items to assist you in your documentation gathering:

FCC Exhibits:

Item 1:  FCC ID – XXXYYYYY (XXX = Grantee Code (3 or 5 characters as assigned by FCC); YYYY = Product Identifier (maximum of 14 characters) – The grantee code must be obtained from the FCC, and it is company and address specific (this code identifies you and you only).  The product identifier is chosen by the grantee.  It may be a maximum of 14 characters, and may include the dash (-) but no other symbols; just alphanumeric characters.  The agent/grantee may obtain this code, however there are pitfalls that may arise.  ACB will obtain this for you at a small charge.  However, if you do not wish us to do that, please refer to

https://acbcert.com/documents/misc-docs/Memorandum-Regarding-FCC-and-ISED-Labeling-Format.pdf to download some helpful hints to try and avoid these possible stumbling blocks.

(continued)

NOTE:  When you obtain the grantee code you will also receive a Grantee Code Registration Number (GCN#).  Please keep this for your records because it will definitely be needed for other transactions with the FCC.

Item 2:  FCC Registration Number (FRN) – Please provide a FRN number for your manufacturer/applicant.  This is now required for all Grantees (reference MD Docket No. 00-205).  To obtain an FRN online, visit the FCC’s Web site at www.fcc.gov and click the Commission Registration System (CORES) link.  For further assistance, please either refer to the FAQ at this same link, contact the CORES helpdesk at CORES@fcc.gov, or call the CORES helpdesk toll-free number:  1-877-480-3201.

Item 4:  Agency Authorization Letter – See attached example.  Must be prepared on applicant/manufacturer letterhead unless there is an agency agreement with the agent company.

Item 5:  Theory of Operation/Technical Description - A brief description of the circuit functions of the device along with a statement describing how the device operates; to include a description of the ground system and antenna, if any, used with the device. (Catalogue sheet may contain most information. It is necessary that this be in a separate document - PDF preferably).   May be held confidential if included in Confidentiality Request.

Item 6:  Tune-Up Procedure – Procedure for ensuring the device is tuned to the correct frequency/frequency range and that it is operating at proper level.  May be held confidential if included in Confidentiality Request.

(continued)

Items 7 and 8:  FCC ID Label and Location - A photo or drawing showing the identification label clearly (you must be able to see the FCC ID number), and the location on the device. These may be submitted as one document demonstrating both, or two separate documents (again preferably PDF).

Information to be included on the label:

The term “FCC ID:” must be included prior to the XXXYYY and all must be contained 		on one line and legible (it is recommended that the type be 6-point or larger).

If product is larger than “palm-sized” (or 8x10cm), the statement according to Section 		15.19 (a) must be included on label (15.19 (a) (1) or (2) or 3) depending on device).

If product is smaller than “palm-sized” (or 8x10cm), the required statement may be 		included in the User’s Guide/Owner’s Manual.

In addition, pursuant to Section FCC 15.19(b)(5) information regarding the label 			material and method of permanent attachment to the product should be supplied, i.e. the 		label must not be paper, and the ink and label material must be a quality and type that 		must last the life of the device.

Label Location:

In addition to being visible to the consumer, the label cannot be located on a removable 		part, such as a battery cover.

Item 9:  User’s Manual/Installation Instructions - A draft copy of the instructions may be submitted if the actual documentation is not available. The actual document shall be furnished to ACB when it becomes available.  Modules require specific verbiage – please inquire further if this applies to your device.

Information to User (From the FCC Rules) - to be included in the user’s manual:

a.  Section 15.19 statement – If device is smaller than the palm, this may be included in manual.

b.  Section 15.21 statement (for all intentional and unintentional radiators)– “Changes or modifications not expressly approved by the manufacturer could void the user’s authority to operate the equipment”.

c.  Section 15.25 Info (if applicable)

d.  Section 15.27 Info (if applicable)

e.  Section 15.105 statement (for digital devices)

f.  Modules (Instructions for installation by the “assemblers” as to method of ensuring proper separation distance between module and antenna and user.

g.  RF Exposure info (if applicable) - See 2.1093 of the FCC Rules

FCC Part 18 devices - To be included in the user’s manual or on packaging if manual is not provided (ex. Some ISM equipment):  Section 18.213 Information.

(continued)

Item 10:  Block Diagram – See Section 2.1033(b)(5) – Exhibit must show “…frequency of all oscillators in the transmitter portion of the device .  The signal path and frequency shall be indicated at each block.  The tuning range(s) and intermediate frequency(ies) shall be indicated at each block.” Document must be separate from manual, and preferably a PDF document.

Item 11:  Schematics – Schematics and description for ALL circuitry and devices provided for determining and stabilizing frequency, for suppression of spurious radiation, for limiting modulation, and for limiting power.  NOTE:  Please ensure that the components and component values are legible on the schematics.  Also, if the EUT has many PC boards, be sure to title each page.  Please provide as ONE legible PDF document.  This exhibit may be held confidential if included on the Confidentiality request letter.

Item 12:  Parts List – Parts list for the radio device, listing all components and/or identifying the source of OEM modules.  This exhibit may be held confidential if included on the confidentiality request letter.

Item 13:  Confidentiality Request Letter (examples are downloadable as stated in item #13 on page 1 of this document) – The exhibits provided to the FCC are accessible by the public on their site.  A special request letter must be submitted to FCC for confidentiality to be granted to certain exhibits.  Both permanent confidentiality (only specific documents allowed – schematics, block diagrams, parts lists, tune-up procedure, operational/technical description) and short-term confidentiality (certain documents are allowed to be held confidential for a maximum of 180 days as long as device is not being marketed)  The documents allowed to be held short-term confidential are external and internal photos, test photos, block diagrams, schematics, user’s manual, parts list, tune-up procedure and operational description.  Under short-term confidentiality, you must request an extension before the end of the initially requested time frame if you still require this service, for a total of 180 days.

Also, if you market before the requested STC timeframe is over, you must notify the FCC to lift the short-term confidentiality. Please see examples that are downloadable from ACB site (as mentioned in item #13, page 1).  NOTE:  In special cases where manufacturer and applicant are different entities, 3rd party confidentiality agreements can be made.  Please contact us for specific details.

Item 14 and 15:  External Photos and Internal Photos - EUT photos, internal and external, showing all faces of the device and all circuitry, and one shot per page. Photos shall show top and bottom of each circuit board, also with shields eliminated.  Internal photos shall show the component placement on the chassis and the chassis assembly.  If components are covered by an insulator, provide a photo with the cover on, and one with the cover removed. External photos shall show the overall appearance, the antenna used with the device (if any), and the controls available to the user.  Please provide as ONE legible PDF document for internal photos and ONE for external photos.

(continued)

Item 16:  Report of Measurements – The technical report must show compliance with pertinent technical requirements.  This report shall identify FCC or Industry Canada test procedures used, dates the measurements were made, location where made, and device tested (model and serial number is available).  Also report shall include sample calculations showing how the measurement results were converted for comparison with the technical requirements.  The report should also include any justifications for testing modifications or omissions.

Item 17:  Test Setup Photos - Test setup photos must show peripheral or accessory devices connected or installed at time of testing, and a brief description of these peripherals and accessories shall be included with test report.  Also please provide photos as a separate document (preferably PDF).

ISED Exhibits (in addition to the above list):

Item 21:  ISED ID – Required for all Category I devices.  The Company Number (obtained from ISED) followed by UPN (unique product number) up to 11 characters. Just as with the FCC Grantee Code, ACB can obtain the number for you, or you may obtain it yourself.  To obtain your own number, you must first register on ISED’s site at:

https://strategis.ic.gc.ca/cgi-bin/allsites/registration-inscription/mainScreen.cgi

Once registered you will need to log in on ISED’s site at:

https://strategis.ic.gc.ca/app/scr/sitt/reltel/dsplyLgn.do?lang=eng

and then use the “Manage Company Information” button followed by the

“Obtain new company number” Link.  This should be done prior to filing applications for certification.  Provide the full company name, Address, City, Province/State, Postal/Zip Code (N/A outside North America), Country, Contact Name, Contact’s Phone Number, Contact’s Email Address, Company Fax Number, and Website URL.  Note that only ISED can issue this number.

Item 24:  Agency Authorization Letter (Example is part of ISED application letters)

Item 25:  RSS-102 Attestation (if applicable to device) – Declaration must be made by a lab qualified to do so.  (Example is part of ISED application letters)

(continued)

Item 26:  Appropriate RF Exposure Warning Statement for User’s Manual:

Excerpt RSS-102:

The applicant is responsible for providing proper instructions to the user of the radio device, and any usage restrictions, including limits of exposure durations. The user manual shall provide installation and operation instructions, as well as any special usage conditions, to ensure compliance with SAR and/or RF field strength limits. For instance, compliance distance shall be clearly stated in the user manual.

The user manual of devices intended for controlled use shall also include information relating to the operating characteristics of the device; the operating instructions to ensure compliance with SAR and/or RF field strength limits; information on the installation and operation of accessories to ensure compliance with SAR and/or RF field strength limits; and contact information where the user can obtain Canadian information on RF exposure and compliance. Other related information may also be included.

More information may be found in RSS-102 which may be down loaded at https://www.ic.gc.ca/eic/site/smt-gst.nsf/eng/sf01904.html and Canada’s Safety Code 6 which more information may be obtained at

https://www.canada.ca/en/health-canada/services/health-risks-safety/radiation/occupational-exposure-regulations/safety-code-6-radiofrequency-exposure-guidelines.html.

Item 27:  Canadian Point of Contact letter - (must be located within Canada) This POC may be authorized agent or distributor.  Please include name of contact, company name, company number, phone number, email, mailing address as part of the Attestation Letter.  (Example is part of ISED application letters)

Item 28:  ISED ID Label Artwork (May be same label from FCC documentation to include ISED ID number).  NOTE that despite the name change from IC to ISED, the correct format is still preceded by “IC:”.  Example:

IC:  XXXX-YYYYYYYYYYY (XXXX denotes manufacturer company number and YYYYYYYYYYY denotes unique product number limited to eleven alphanumeric characters.)

COMPOSITE DEVICES SUBJECT TO OTHER FCC RULE SECTIONS OR ISED STANDARDS - In addition to the above, refer to the additional FCC rule section or ISED standard applied for (if other than those listed above), for other specific requirements.

NOTE:  This is the minimum set of documents that will be required for TCB review.  Specific rule requirements may have additional requirements that need to be addressed as well.