## Slide 1: ACB Module Assessment and Integration FCC and IC
Michael Derby
ACB Europe 7 April 2014

## Slide 2: Introduction
Modules
  Why do we always discuss modules?
  Modular Approvals (assessing the module)
    Including Limited Modular Approvals
  Using approved modules (Integrating modules)
  USA and Canada
  This presentation is of the basic fundamentals
  I will not cover RF Exposure in detail 
    But I will mention it

## Slide 3: Why modules?
A change in Industry
  Radio boffins, no more
  It’s a wireless world
    Buy a pre-approved module
    Integrate modules into hosts
    Entrepreneurs and marketing people
    Laptops with WWAN, WLAN and Bluetooth
  A challenge for our industry

## Slide 4: Modular Approval Types
Some examples:
A radio module to be approved for use in any host and sold to anyone
  The transmitter module is fully assessed to all the requirements
  The module is intended for any environment
    Within the scope of the certification parameters
  In certification terms, this is known as: Full or Single Modular Approval

## Slide 5: Modular Approval Types
A radio module to be approved for use in a specific host or environment and used under control of the module manufacturer
  The transmitter module is assessed to specific, applicable requirements
  The module is intended for a use or an installation in specific environment(s)
  In certification terms, this is known as: Limited Modular Approval

## Slide 6: Modular Approval Types
A series of similar devices require certification and they share a common radio module or radio circuitry
  The transmitter module is assessed to applicable requirements, for use with hosts
  The module is intended for those specific hosts and environments
  In certification terms, this is known as: Limited Modular Approval

## Slide 7: FCC Modular Approval
Modular Approval
  The Module will have the FCC ID
      The module must be labelled with the FCC ID
  Any host incorporating the module will show that the module is contained within it
    Contains FCC ID: XXXYYYYY
    FCC ID will relate to module, not host
  Modular Approval is defined in Part 15.212
    Part 15 C, which is unlicensed intentional radiators
      Licensed devices do also get certified as modules

## Slide 8: FCC Modular Approval
Technical, administrative, testing and certification requirements for Modular Approval
  A set of criteria exist for getting full Modular Approval certification and allowing the module to be used in any host
  If you do not meet all criteria, then you cannot achieve full Modular Approval
  Modular Approval criteria shown on the next page:

## Slide 9: FCC Modular Approval
Eight criteria for Modular Approval (15.212)
  Transmitter must have its own shield
  Must have buffered modulation/data inputs
  Must have power supply regulation
  Must meet Part 15 antenna requirements
  Must be tested in stand-alone configuration
  Must be labelled with the FCC ID
  Must meet its own FCC rule part
  Must meet RF Exposure requirements

## Slide 10: FCC Modular Approval
Eight criteria for Modular Approval (15.212)
  During the certification application, provide a cover letter to explain compliance with all eight requirements in 15.212
  You cannot exclude one of the eight and hope it’s ok
    “But we pass the tests, even without a shield!”
    “But it only operates when it’s inside the host!”
  It’s a clear certification process
    Or, it is Limited Modular Approval

## Slide 11: FCC Integrating Modules
Using a compliant module
  Rely on certification of the module for compliance
  The host must state that it contains the module and the host must show the module’s FCC ID
  You do not get certification of the host, based on the certification of the module
  You must follow the module’s Grant limitations
    Distance and co-location for RF Exposure
  Host must still comply with its own requirements
    For example, Part 15B, Verification or DoC
      And 15.5 !

## Slide 12: FCC Integrating Modules
Using a compliant module
  May need to work with module manufacturer
    If co-location or SAR is a problem on module’s Grant, they may need to change their Grant
  Responsibility for compliance remains with the module Grantee, even after installation
    This is why the module’s installation instructions are so very important
    FCC gets calls “I bought a module, what do I do?”
      This should not happen!

## Slide 13: FCC Integrating Modules
User Installation of the module
  Manufacturer selling a certified module for installation by a user, not an installer
    Two Way authentication technology may be required to only allow module operation in acceptable hosts (such as for RF Exposure)
    A Bios Lock is an acceptable example of this

## Slide 14: FCC Limited Modular Approval
If it doesn’t meet all eight criteria, it could get “Limited Modular Approval” for a specific host
  If the host or end environment is known, Limited Modular Approval ‘may’ be possible
    Limited to application
    Limited to host
    Limited to installer (typically Grantee or partner)
    There are differences in test method
    There are differences in certification process

## Slide 15: FCC Limited Modular Approval
You can’t just sell an LMA module to anyone, as if it had full Modular Approval
    That’s the whole point of modular approvals!
    You can’t miss one of the eight, so call it LMA and sell it as if it was a fully certified module
  The Grantee is always responsible for compliance in any host, full or limited module
  Can’t rely on OEM to re-test in their host
LMA means that limitations exist

## Slide 16: FCC Limited Modular Approval
The LMA module will be certified for a range or series of devices, similar in construction
  The LMA module will be certified for use in that range or series of devices only
  Compliance with that range of hosts will have been demonstrated, no other hosts covered
    Additional host series can be added through PC
  The module is tested in (with) the host or a representative of the series of hosts

## Slide 17: FCC Limited Modular Approval
The LMA module will be certified for use by the Grantee or an authorised OEM
  The Grantee must maintain control of the installation, so typically installation is only permitted by the Grantee
  Installation by an OEM may be permitted, for example if there is a contractual agreement
    OEM must understand the limitations of installation
    It is more than simply following the Grant notes

## Slide 18: FCC Limited Modular Approval
The LMA module will be tested in a representative host
  The LMA does not meet all eight criteria, so it must show that it can comply when in the host
    Cross-coupling if no shield
    Voltage input if no regulator
    Data input if no buffer
  The LMA should not be tested stand-alone
  Dissimilar hosts may require separate testing

## Slide 19: FCC Limited Modular Approval
The device will be certified under the title: Limited Modular Approval
  The Grant notes will describe the series of hosts and/or limitation(s) of use
  The filing will list all hosts and/or conditions permitted for that module

## Slide 20: Split Modular Approvals
RF transmission (radio front-end) is separate from the control element
  These are called Split Modules
  These can be certified by TCB with a PBA
  Modules where the transmitter firmware is held on a host, is a split module
    Even bespoke software supplied with module, such as files downloaded at each start-up

## Slide 21: FCC Licensed Modules
Licensed devices do get Modular Approval
  Modular Approvals are contained in Part 15C and therefore only for unlicensed devices
  It is possible to certify a licensed module, with ‘Modular Approval’
    Split Modular is not permitted for Licensed Devices
  The eight criteria of 15.212 may be used as a guide but are not mandatory
  Expect changes, possibly this week!

## Slide 22: FCC Licensed Modules
Requirements for Licensed Modular Approval
  Testing and cover letter justification must demonstrate compliance
  Clear instructions must be provided to OEM or other installers, to define Grant conditions; installation requirements and need for a license
  Instructions for placing the FCC ID on the host must be supplied to the installer (electronic is ok)
  The Grantee is always responsible for compliance in the end host installation

## Slide 23: Useful Module KDB
If you are in the module business
  Sleep with KDB 996369 under your pillow
  KDB 784748 contains labelling requirements
  KDB 447498 contains RF Exposure, MPE and SAR test guidance
  KDB 616217 contains SAR host guidance

## Slide 24: IC Modular Approvals
Canada has Modular Approval
  RSS-GEN section 3.2 contains information
  Requirements and Labelling similar to FCC
    The module must show the IC number
    The module must show the model (“Model: “)
    The host label states: Contains IC: XXXX-YYYYY
      The host label does not need to show the module’s model number
    FCC will allow an electronic version of the module’s ID on the host and IC is considering it

## Slide 25: IC Modular Approvals
Canada has Modular Approval
  The eight technical criteria are very similar
    A letter must be supplied during application
    Letter must be for RSS-GEN, not for FCC 15.212
  For IC, Licensed Modules use the same eight criteria as Unlicensed Modules, unlike FCC
    We expect the FCC to add licensed modular in an NPRM to be announced in April 2014

## Slide 26: IC Modular Approvals
Canada has Limited Modular Approval too
  RSS-GEN section 3.2.3 contains information
    Similar to FCC Limited Modular Approvals
    Same approach to be followed

## Slide 27: IC Modular Approvals
Modular approvals, RSS-GEN, section 3.2
  Host label must reference the module’s IC number but not the Model number

## Slide 28: RF Exposure
RF Exposure for the FCC and IC
  Mobile Devices
    More than 20cm from any user
    Typically a calculation based on output power
    Quite a general, calculation assessment
      Based on power and distance
  Portable Devices
    Less than 20cm from a person
    This is an exact measurement of a specific product
      Antenna, enclosure, configuration specific

## Slide 29: RF Exposure
  Most modules are therefore Mobile
    MPE assessment at 20cm
    Calculation based on output power and antenna gain
      With modules, antenna gain may not be known
      Worst case values might be used
    Grant Notes state that the module is “Mobile”
      More than 20cm from users
        There is a power threshold to trigger a SAR assessment
      Must not co-locate with other transmitter antennas
        “Except in accordance with FCC procedures”
        Common use of a Class 2 Permissive Change

## Slide 30: RF Exposure
  Most modules Mobile
    Modules may be co-located in real installation
      Transmit antennas within 20cm of each other
      Transmit at the same time
    Co-Location can be handled theoretically at the time of certification for the Module
      Even if future co-locations are not known
      Typical co-location scenarios
        Examples
      Grant notes state “No co-location, except as detailed in filing”
    Any co-location which has been calculated at the time of certification would not require a Permissive Change

## Slide 31: RF Exposure
  It is possible to certify a module as Portable
    If the output power of the module is below the power threshold to allow Portable use without SAR testing
      Section 4.3 of KDB 447498
    Based on maximum transmitter output power, antenna distance from user, and transmitter frequency
      This could allow Portable use in any host
      May need installation control and/or professional installation
        Power to be added to other modules for co-location
    If output power of the module is above the power threshold to allow portable use without SAR testing
      Then SAR testing of the module could be possible!

## Slide 32: RF Exposure
  It is possible to certify a module as Portable
    SAR test on the module with an antenna
      Limitations are based on SAR result
    Lower SAR result allows greater flexibility
      <0.4 W/kg = any host
      <0.8 W/kg = any range of suitable hosts
      <1.2 W/kg = single platform type
      <1.4 W/kg = re-test for any host
    SAR is specific to antennas
      Only certified for use with tested antenna(s)
        Other antennas through Class 2 Permissive Change
    Grant notes list SAR and hosts

## Slide 33: RF Exposure
  Mobile Module into a Portable Host
    Module certified as Mobile at >20 cm
    Installer wishes to put into a Portable Host
      The Grant notes might say “more than 20cm”
    Is the output power above the threshold?
      If not, then SAR is not required
    If power is above threshold, then SAR testing needed
      Perform SAR test on host and module combination
      Module Grantee to complete a Class 2 Permissive Change
    If host uses proximity sensors
      Module will require new FCC certification with that host
        And agreements with OEM

## Slide 34: Modules
  Good luck!

## Slide 35: Questions?
Contacts:
  michaeld@acbcert.com
  www.acbcert.com